## Slide 1: ADC in theorie en praktijk
Bart Bozon

## Slide 2
Wat is het?
Resolution, sample frequency...
Nyquist
Aliasing
Successive Approximation Register ADC
Andere types
Quizzzzz

## Slide 3
ADC staat voor Analog-to-Digital Converter
Een ADC zet een analoog signaal (zoals een spanningsniveau) om in een digitaal getal dat een computer of microcontroller kan begrijpen.

## Slide 5
The ESP32-WROOM module integrates two 12-bit SAR (Successive Approximation Register) Analog-to-Digital Converters (ADCs) with a total of 18 measurement channels. These ADCs can measure analog voltages within a specified range, and their digital output is represented by 12 bits, resulting in 4096 discrete values.

## Slide 7
Sample time =
Sample frequency
Sample resolution

## Slide 12
Harry Nyquist
Om een analoog signaal volledig en correct digitaal te kunnen reconstrueren, moet je het signaal bemonsteren met een frequentie die minstens twee* keer zo hoog is als de hoogste frequentiecomponent in dat signaal.
Dit minimum wordt de Nyquist-frequentie genoemd.
* doe maar 3 of 4 keer!!!

## Slide 13
Wat is de sample rate (=frequentie) van cd’s?
En waarom?
En MP3’s?

## Slide 15: Aliasing

## Slide 16
Anti Alias filter
Reconstructie filter

## Slide 17
Anti Alias filter
Reconstructie filter
HOE?

## Slide 18
Anti Alias filter
Reconstructie filter
HOE?

## Slide 20
The ESP32-WROOM module integrates two 12-bit SAR (Successive Approximation Register) Analog-to-Digital Converters (ADCs) with a total of 18 measurement channels. These ADCs can measure analog voltages within a specified range, and their digital output is represented by 12 bits, resulting in 4096 discrete values.

## Slide 21
https://www.monolithicpower.com/en/learning/mpscholar/analog-to-digital-converters/detailed-analysis-of-adc-architectures/sar-adcs?srsltid=AfmBOoqg18Vjq_k_TZNTkb2FBp00_URdZctyW9Nv34VrKq7yNZzE86VW
Sample & Hold
Digitaal -> Analoog

## Slide 23
https://www.monolithicpower.com/en/learning/mpscholar/analog-to-digital-converters/future-trends-and-challenges-in-adcs/novel-adc-architectures

## Slide 24
WOOCLAP QUIZZZZ!!!

## Slide 25
Questions?